## Slide 1: ΕΦΑΡΜΟΓΕΣ ΕΠΙΧΕΙΡΗΣΙΑΚΗΣ ΕΡΕΥΝΑΣ
Ενότητα 2: Scheduling of Loading and Unloading of Crude oil in a Refinery
Γεώργιος Κ.Δ. Σαχαρίδης
Τμήμα Μηχανολόγων Μηχανικών
ΠΑΝΕΠΙΣΤΗΜΙΟ ΘΕΣΣΑΛΙΑΣ

## Slide 2: Refinery
A refinery is a system composed of docks, pipelines, a series of tanks to store the crude oil (and prepare the different blends), CDUs, VDUs production units, blenders and tanks to store the raw materials and the final products.

## Slide 3: The Problem
Once the quantities and the types of crude oil required are known, schedulers must schedule the loading and unloading of tanks. The problem that arises then is how to schedule the transfer of crude oil from the docks to the tanks and from the tanks to the CDUs/VDUs, minimizing the setup cost of the system.

## Slide 4: Refinery
Στο σχήμα βλέπουμε μια τυπική διάταξη από ένα Oil Refinery. Δεξαμενόπλοια
έρχονται στις αποβάθρες, ξεφορτώνουν το πετρέλαιο στις δεξαμενές, το οποίο
πετρέλαιο στην συνέχεια περνάει από τις εγκαταστάσεις δυίλισης.

## Slide 5: Typical Refinery
A typical refinery is composed of 1 to 10 tanks for the storage of the crude oil, 2 to 4 CDUs/VDUs and 1 or 2 docks, which can accommodate 4 to 5 vessels per month.
The storage capacity of each tank can range from 80000 m3 to 150000 m3. Crude oil flows from the docks to the tanks, and its flow depends on the unloading capacity of the boats, ranging from 1000 m3/hour to 5000 m3/hour. Duration of a boat’s unloading is typically defined a priori by contract (ex. 36 hours).
Each CDU/VDU has a distillation capacity that can range from 200 m3/hour to 2000 m3/hour.

## Slide 6: Refinery
A refinery is a system composed of docks, pipelines, a series of tanks to store the crude oil (and prepare the different blends), CDUs, VDUs production units, blenders and tanks to store the raw materials and the final products.

## Slide 7: The Problem
Once the quantities and the types of crude oil required are known, schedulers must schedule the loading and unloading of tanks. The problem that arises then is how to schedule the transfer of crude oil from the docks to the tanks and from the tanks to the CDUs/VDUs, minimizing the setup cost of the system.

## Slide 8: Data of the system
Dimensions of the refinery;
Arrival dates of vessels based on medium-term planning,
Demand of crude oil by the CDU/VDU;
Initial conditions (quantity and composition in each tank) and the system’s capabilities (operational times, tanks capacity and flow limits);

## Slide 9: Data of the system
The number of tanks available for storage and their storage capacity are known;
The production rates;
The recipe preparation alternative;
The blending mode.

## Slide 10: Modeling
Continuous and binary decision variables:
  The continuous variables correspond to flows from docks to tanks, flows from tanks to CDUs/VDUs, and quantities stored in the tanks.
  Binary variables are used to specify connections between docks and tanks, connections between tanks and CDUs /VDUs, and also the availability and setup for loading and unloading of the tanks.

## Slide 11: Modeling
The constraints necessary to describe the system include:
  a) satisfying operations rules;
  b) satisfying material balances;
  c) meeting storage capacity constraints;
  d) satisfying blend properties;
  e) establishing a connection between docks and tanks;
  f) establishing connections between tanks and CDUs/VDUs; and
  g) setup of tanks for loading or unloading.

## Slide 12: Reference example
The system under study is composed of two docks, six tanks for the loading of crude oil, and two crude distillation units (CDU) fed by these six tanks;
The unloading time of a boat is equal to 36 hours and fixed by contract with the suppliers of crude oil;
The distillation flow for the two CDUs are 270-350 m3/hour for CDU1 and 300-1660 m3/hour for CDU2;
The blends are prepared using the pipelines just before the CDUs.

## Slide 13: Reference example
The period of planning is equal to 30 days (720 hours);
The arrival plan of three boats (when, which type, and what quantity of the crude oil they carry) is known a priori;
The demand of 12 different blends (composed of a maximum of three different types of crude oil) by the two CDUs (when, which type, and what quantities of blend) is given;
The initial state of each tank at the beginning of a scheduling period and their storage capacity is given(100000 m3).

## Slide 14: Reference example
Το σχήμα έχει 3 παράλληλες γραμμές που απεικονίζουν τον χρονικό ορίζοντα:
Αφίξεων των δεξαμενόπλοιων
Ζήτηση σε πετρέλαιο ανεξαρτήτως τύπου για κάθε μονάδα διύλισης

## Slide 15: Reference example
The objective is to minimize the setup cost of six tanks for the unloading of three boats, which arrive at precise hours, while preparing the 12 blends requested and unloading them towards the CDUs when appropriate.

## Slide 16: Why setup cost is important?
The setup of tanks, involving loading the quantities of crude oil at the docks and unloading the quantities of blends or crude oil toward the CDU/VDU, requires a series of operations that are expensive for the refinery.

## Slide 17: Why setup cost is important?
The most critical and expensive operations associated with a tank’s setup at each stage are:
  Before loading/unloading:
    Configuring the pipeline network (e.g. opening of valves, configuration of pumps, etc.);
    Filling pipelines with crude oil which is a dangerous and lengthy procedure;
    Sampling of crude oil for chemical analyses;
    Measuring of the crude oil stock in tank before loading/unloading;
    Starting the loading/unloading; and
    Stopping the loading/unloading.

## Slide 18: Why setup cost is important?
The most critical and expensive operations associated with a tank’s setup at each stage are:
  After loading/unloading:
    Configuring the pipeline network which is a dangerous and lengthy procedure (e.g. closing of valves, configuration and maintenance of pumps, etc.);
    Emptying of pipelines; and
    Measuring the crude oil loaded/unloaded in the tanks.

## Slide 19: Why setup cost is important?
Costs associated with these operations require that the loading and unloading of tanks be completed with the minimum number of setups.
The minimization of the number of setups is required also for security reasons, as the above operations are complicated and with each start of a new loading and unloading, the system is strained.

## Slide 20: Current practice – Heuristic approach
Currently, the obtained schedule is generated based on managerial experience and on manual calculations giving rise to a unique optimal schedule for each period, separately taking into account all the constraints and minimizing the number of the tanks used.
This type of optimization gives for the reference example a sub-optimal solution (feasible solution), leading to twenty-five setups.
These 25 setups of six tanks are required for the loading of crude oil quantities transferred by the three boats and the tank unloading, in order to satisfy the request of 12 different blends by the two CDUs.

## Slide 21: General context of scheduling of crude oil
The objective is to present a general model which gives the optimal solution for the scheduling of crude oil and can also be used in any equivalent system

## Slide 22: General context of scheduling of crude oil
The potential financial and operational benefits associated with the development of this model are enormous, as an advanced optimization tool for scheduling could allow the refinery to:
a) minimize the flow problems and the loss of crude oil;
b) obtain the optimal periodic plans of production;
c) give direction for the future;

## Slide 23: General context of scheduling of crude oil
d) re-optimize the system in case of stochastic events (ex. accidents, machine failures, new arrivals, changes to distillation schedules); and
e) compare the results obtained from various distinct scenarios. Summarizing loading and unloading of crude oil is one of the most critical activities in a refinery.
Better analysis of this activity gives rise to better use of a system’s resources, as well as improved total visibility and control of production units and of the entire supply chain.

## Slide 24: Main features of the system under study
Blending preparation:
  The different blends could be produced using the pipelines just before the CDU/VDU in a place called the manifold. In this case, only one type of crude oil can be stored in each tank at a time
  The blends required by the CDU/VDU are prepared in the tanks themselves. In this case, a quantity of a given type of crude oil is already loaded in a tank then stored and kept on standby until a quantity of another type of crude oil is unloaded into the same tank, in order to produce the required blend.

## Slide 25: Main features of the system under study
Recipe preparation alternatives:
  The standard recipe preparation. The required blend must satisfy an exact composition of crude before being distilled in a CDU, regardless of blending mode. For example, the blend required by a CDU must contain 20% of crude oil type A and 80% of crude oil type B for an exact, a priori defined quantity.
  The flexible recipe (relaxation of the standard recipe preparation). The components of the required blend must satisfy lower and upper bounds. For example, a CDU requires a quantity of a blend, where type A can constitute at least 20% of the total quantity and not more than 50%.

## Slide 26: Refinery Rules
Rule 1: Physical limitations exist in the system (e.g. tank capacity, flow and pumping rates);
Rule 2: If a given tank is feeding a distillation unit, it cannot be simultaneously loaded and vice versa;
Rule 3: Meet the constraints imposed by the blending type; and
Rule 4: Meet the constraints imposed by the distillation option.

## Slide 27: Mathematical Modeling

## Slide 28: Decision Variable
We consider two types of decision variables (continuous and binary):
  The continuous variables are associated with the flow between docks and tanks, flow between tanks and CDUs/VDUs, and the quantities of various types of crude oil in the tanks.

## Slide 29: Decision Variable
We consider two types of decision variables (continuous and binary):
  The binary variables represent decisions regarding the loading, unloading and setup of a tank (which is necessary either before the loading of a quantity available at the dock or before unloading crude oil or a blend of crude oil towards the CDU/VDU). The binary variables represent decisions regarding the loading, unloading and setup of a tank (which is necessary either before the loading of a quantity available at the dock or before unloading crude oil or a blend of crude oil towards the CDU/VDU). The binary variables represent decisions regarding the loading, unloading and setup of a tank (which is necessary either before the loading of a quantity available at the dock or before unloading crude oil or a blend of crude oil towards the CDU/VDU).

## Slide 30: Mathematical Modeling

## Slide 31: Constraints
Four groups of constraints which guarantee certain operational conditions:
  Constraints which guarantee that the quantities loaded in tanks are equal to the quantities available to docks in each period
  Constraints expressing that the quantities unloaded towards CDUs/VDUs are equal to the quantities required by them
  Constraints expressing the material balance
  Constraints guarantee that quantity stored in a tank is not greater than its storage capacity.

## Slide 32: Constraints applicable in any case
Constraint (1) is a loading constraint and guarantees that the sum of the quantities loaded in tanks, at dock i, for period t, is equal to the quantity available at the dock.
Constraint (2) is an unloading constraint and guarantees that the sum of the quantities unloaded by all the tanks, towards CDUk, for period t, is equal to the quantity required by the CDUk.

## Slide 33: Constraints applicable in any case
Constraint (3) is the material balance constraint expressing that the quantity of crude oil, type j, which is stored in tank z, at period t, is equal to the quantity which was stored at period t-1, plus the sum of quantities of the same type that are loaded for this period by all docks i, less the sum of the quantities unloaded by this tank towards all CDUs.

## Slide 34: Constraints applicable in any case
The capacity constraint is defined by constraint (4) where the sum of different types of crude oil should be less than or equal to the total storage capacity.
Constraints (5-6) are associated with operation rules and express the connection if a flow between a tank z and dock i or CDUk is established for loading or unloading. (Notice that the constant M used in the following equalities takes a value equal to the storage capacity of the tanks.

## Slide 35: Constraints applicable in any case
Constraint (7) guarantees that loading and unloading does not take place at the same time. We notice that the sum over i in constraint (7) results from the fact that a maximum of only one boat unloads crude oil to a tank z in the time period t.
Constraints (8-9) are the setup constraints. These constraints guarantee that during the loading or unloading of a tank z, a setup cost is charged at the beginning of the loading or unloading period.

## Slide 36: Objective Function
The objective function for the developed model is to minimize the total number of tank setups necessary for the loading and unloading of the crude oil.

## Slide 37: Blending in the manifold
When the blend is prepared just before the CDU in the manifold using pipelines, the following decision variables and constraints should be added. The additional decision variable ( ) is a binary variable (0-1) which is equal to 1 if tank z contains type j, for the period t and equal to zero if not.

## Slide 38: Blending in the manifold
Additional constraint should guarantee that only one type j of the crude oil can be stored in a tank z, in the period t and should ensures the coherence between decision variables

## Slide 39: Blending modes – Standard recipe preparation /OM11 - OM12 models
Standard recipe preparation
Flexible recipe preparation

## Slide 40: Blending in tanks
When blend is prepared in the tanks, It is necessary to introduce a new term: the acceptable blend:
Preparation of blend in tank – Standard recipe preparation /OM21 model
  In order that a tank z is unloaded towards CDUk, at period t, the quantity of the j type must be equal to the total quantity which exists in the tank multiplied by the rate required by CDUk. Preparation of blend in tank - Flexible recipe preparation /OM22 model
  In order that a tank z is unloaded towards CDUk, at period t, the quantity of the j type must satisfy the upper and lower bounds of the component j required by the CDUk.

## Slide 41: Blending in the manifold and tanks
When a percentage of the crude oil is unloaded from the tank z, to the CDUk, in period t then all the types of crude oil are unloaded simultaneously in a quantity which satisfies the proportion of the mixture.

## Slide 42: Blending in the manifold and tanks
Standard recipe preparation / OM31 model
  The sum of the quantities unloaded by all the tanks, towards CDUk, for period t, is equal to the quantity required by the CDUk
Flexible recipe preparation / OM32 model
  With the flexible distillation, the additional constraints are that the sum of quantities type j unloaded by all tanks, for period t, towards CDUk satisfies the upper and lower percentage of the quantity required by this CDUk

## Slide 43: Heuristic Optimization vs. Exact Optimization
Example | Model HM11 | Model OM11 | Relative difference | CPU Resolution
Ex.1 | 9 setups | 8 setups | 11.11% | 10h
Ex.2 | 8 setups | 7 setups | 12.5% | 11h
Ex.3 | 14 setups | 13 setups | 7.14% | 13h
Ex.4 | 22 setups | 19 setups | 13.63% | 17h
Ex.5 | 13 setups | 12 setups | 7.69% | 13h
 | Model HM12 | Model OM12 |  | 
Ex.6 | 16 setups | 13 setups | 18.75% | 16h
Ex.7 | 13 setups | 12 setups | 7.69% | 15h
Ex.8 | 20 setups | 15 setups | 25% | 17h
Ex.9 | 23 setups | 18 setups | 21.73% | 19h
Ex.10 | 16 setups | 13 setups | 18.75% | 16h
 | Model HM21 | Model OM21 |  | 
Ex.11 | 23 setups | 20 setups | 13.04% | 16h
Ex.12 | 18 setups | 15 setups | 16.66% | 16h
Ex.13 | 19 setups | 18 setups | 5.26% | 19h
Ex.14 | 35 setups | 30 setups | 14.28% | 22h
Ex.15 | 17 setups | 15 setups | 11.76% | 19h
 | Model HM22 | Model OM22 |  | 
Ex.16 | 33 setups | 26 setups | 21.87% | 19h
Ex.17 | 22 setups | 20 setups | 9.09% | 18h
Ex.18 | 19 setups | 16 setups | 15.78% | 18h
Ex.19 | 22 setups | 17 setups | 22.72% | 17h
Ex.20 | 32 setups | 27 setups | 15.62% | 18h

## Slide 44: Time representation
Το σχήμα έχει 3 παράλληλες γραμμές που απεικονίζουν τον χρονικό ορίζοντα:
Αφίξεων των δεξαμενόπλοιων
Ζήτηση σε πετρέλαιο ανεξαρτήτως τύπου για κάθε μονάδα διύλισης

## Slide 45: Time representation
Το σχήμα έχει 3 παράλληλες γραμμές που απεικονίζουν τον χρονικό ορίζοντα:
Αφίξεων των δεξαμενόπλοιων
Ζήτηση σε πετρέλαιο ανεξαρτήτως τύπου για κάθε μονάδα διύλισης
Ο χρονικός ορίζοντας έχει διαιρεθεί σε χρονικές
ζώνες.

## Slide 46: Event-based time representation
Hourly representation | Event-based representation
Το σχήμα έχει 3 παράλληλες γραμμές που απεικονίζουν τον χρονικό ορίζοντα:
Αφίξεων των δεξαμενόπλοιων
Ζήτηση σε πετρέλαιο ανεξαρτήτως τύπου για κάθε μονάδα διύλισης
Εκτός της διακριτοποίησης του χρόνου, βλέπουμε και την διακριτοποίηση σε περιόδους.

## Slide 47: Reference example - Event based time representation
Παράδειγμα βασιζόμενο στην προηγούμενη αναπαράσταση του χρόνου.

## Slide 48: Size of the mathematical models

## Slide 49: Linearization of constraints
Modeling with bilinear products of continuous and 0-1 decision variables

## Slide 50: Linearization of constraints

## Slide 51: Linearization of constraints
The above formulation corresponds to a nonlinear model where we have a bilinear product of continuous and general integer variable. In order to apply the above method we need a preprocessing step. The general integer variable should be expressed as a function of auxiliary binary variables leading to new bilinear product of binary and continuous variables:

## Slide 52: Linearization of constraints

## Slide 53: Linearization of constraints